MOD FORM 2205

SCHEDULE OF INSPECTIONS (For New Installations Only)

| Site: | Building: |
| --- | --- |
| Methods of protection against electric shock | Prevention of mutual detrimental influence |
| Both basic and fault protection: |  | (a) | Proximity to non-electrical services and other influences |
|  | (i) | SELV |  | (b) | Segregation of Band I and II circuits or use of Band II insulation |
|  | (ii) | PELV |  | (c) | Segregation of safety circuits |
|  | (iii) | Double insulation | Identification |
|  | (iv) | Reinforced insulation |  | (a) | Presence of diagrams, instructions, circuit charts and similar information |
| Basic Protection: |  | (b) | Presence of danger notices and other warning notices, including that they are securely fixed, durable and legible |
|  | (i) | Insulation of live parts |  | (c) | Labelling of protective devices, switches and terminals |
|  | (ii) | Barriers or enclosures |  | (d) | Identification of conductors |
|  | (iii) | Obstacles |  | (e) | Fitted at the point of connection to every earthing conductor, and earth electrode, the main equipotential bonding and the points of every bonding conductor to every extraneous conductive part. |
|  | (iv) | Placing out of reach |  |  |  |
| Fault Protection: | Cables and conductors |
| (i) Automatic disconnection of supply: |  |  | Selection of conductors for current-carrying capacity and voltage drop |
|  |  | Presence of earthing conductor |  |  | Erection methods |
|  |  | Presence of circuit protective conductors |  |  | Routing of cables in prescribed zones |
|  |  | Presence of protective bonding conductors |  |  | Cables incorporating earthed armour or sheath, or run within an earthed wiring system, or otherwise adequately protected against nails, screws and the like |
|  |  | Presence of supplementary bonding conductors |  |  |  |
|  |  | Presence of earthing arrangements for combined protective and functional purposes |  |  | Additional protection provided by 30mA RCD for cables concealed in walls (where required in premises not under the supervision of a skilled or instructed person) |
|  |  | Presence of adequate arrangements for other sources, where applicable |  |  |  |
|  |  | FELV |  |  | Connection of conductors |
|  |  | Choice and setting of protective and monitoring devices (for fault and/or overcurrent protection) |  |  | Presence of fire barriers, suitable seals and protection against thermal effects |
| (ii) Non-conducting location: | General |
|  |  | Absence of protective conductors |  |  | Presence and correct location of appropriate devices for isolation and switching |
| (iii) Earth-free local equipotential bonding: |  |  |  |
|  |  | Presence of earth-free local equipotential bonding |  |  | Adequacy of access to switchgear and other equipment |
| (iv) Electrical separation: |  |  | Particular protective measures for special installations and locations |
|  |  | Provided for one item of current-using equipment |  |  |  |
|  |  | Provided for more than one item of current-using equipment |  |  | Connection of single-pole devices for protection or switching in line conductors only |
| Site: | Building: |
| Additional protection: | General (Cont.) |
|  |  |  | Correct connection of accessories and equipment |
|  |  | Presence of residual current device(s) |  |  | Presence of undervoltage protective devices |
|  |  | Presence of supplementary bonding conductors |  |  | Selection of equipment and protective measures appropriate to external influences |
|  |  |  |  |  | Selection of appropriate functional switching devices |
| Functioning and Condition |
| Correct Functioning of : |  |  |  |
|  | (i) | Circuit Breakers |  | (vii) | Meters |
|  | (ii) | RCD |  | (viii) | Instruments |
|  | (iii) | Relays | Condition: |  |
|  | (iv) | Switches |  | (i) | Tightness of all Connections, including integrity of main and supplementary bonding. |
|  | (v) | Push Buttons |  | (ii) | Integrity of locks and seals |
|  | (vi) | Contactors |  |  |
| QUALITY ASSURANCE |
| I hereby certify that the information for the specified building contained in this MOD FORM 2205 is correct to the best of my knowledge and compliant with the relevant regulations. Name (BLOCK CAPITALS): Signature: Date: |

Notes:

(	to indicate an inspection has been carried out and the result is satisfactory

N/A	to indicate that the inspection is not applicable to a particular item

An entry must be made in every box

- SELV An extra-low voltage system which is electrically separated from Earth and from other systems. The particular requirements of the Regulations must be checked (see BS7671 Regulations 414)

- Method of basic protection - will include measurement of distances where appropriate

- Obstacles - only adopted in special circumstances (see BS7671 Regulations 417.1 and 417.2)

- Placing out of reach - only adopted in special circumstances (see BS7671 Regulations 417.1 and 417.3)

- Non-conducting locations - not applicable in domestic premises and requiring special precautions (see BS7671 Regulation 418.1)

- Earth-free local equipotential bonding - not applicable in domestic premises, only used in special circumstances (see BS7671 Regulation 418.2)

- Electrical separation (see BS7671 Section 413 and Regulation 418.3)

# Footnotes

Single pole switches are not allowed in accordance with JSP482 Chapter 8 and if found shall be replaced with alternatives which disconnect each live conductor.