Multi-Purpose Personal Protection System (MP3S)
User Requirements Document
Industry Engagement Release 2
Version 1.0

Introduction

Purpose of Document

This document sets out the user requirements for the Multi-Purpose Personal Protection System (MP3S). This is a consolidated set of requirements that is relevant to the Police, Fire, Health and MoD. All requirements, priorities and measures of effectiveness have been agreed with requirements leads from each organisation.

Included within this document is the operational context, the user requirements and a glossary of terms used within the requirements.

Priority Definitions

Each requirement has been prioritised according to the following definitions:

Priority	Definition
Mandatory	Legislative requirements.
Key	These are the top requirements which define the purpose and main aims of the protection system. These cannot be traded out under any circumstances as without these, the protection system is not fit for purpose and the project will fail. If these requirements are not met by manufacturer submissions they will not be taken any further forward.
Highly Desirable	These requirements are also required to be met and cannot be traded out without a significantly good reason that has been agreed by the MP3S Project Board. These requirements can be weighted for the evaluation of submissions. If these requirements are not met by manufacturer submissions they can still be looked at further to identify potential work-around of trade-offs.
Desirable	It is possible to trade out these requirements without significant impact on the desired outcomes and the decision can be made at the MP3S Requirements Board level.
Future	Not required at present but useful to include during development to inform future upgrades and design of the system.

Operational Context
The multi-purpose personal protection system (M3PS) is intended for all responders deployed to incidents where protection from chemical, biological, radiological or nuclear materials may be required. Most normal duties undertaken by these responders are required to be performed in such incidents, and the following narrative is intended to provide an overview of this.

The fire, police, ambulance and military communities are taking a coordinated approach in providing future CBRN protection requirements from a multi-agency perspective. This paper outlines the operational scenarios for which the protective system is required by these responders: it may be a single ‘ensemble’ or may comprise a number of elements used in combination or permutation.

Responders may be required to attend a suspected CBRN event at short or no notice. They may be called in from home or redeployed from a variety of different duties which could include patrol on foot or in a vehicle or work in an office or other building. Some will respond as individuals to a notified rendezvous point (RVP), others will form groups elsewhere and then travel to an RVP[1].
[1] Ensembles may need to be stored singly or in small multiples for individuals at home or work, or in bulk by ensemble or component parts for storage or for transport to a scene.

On arrival at an RVP or holding area or as part of a planned deployment, there is the potential for responders to be held, potentially for several hours or a full tour of duty prior to deployment in full protection. Depending on the notice period that responders will get before being required to be deployable as fully protected, they may need to wear some of the PPE to give the ability to be fully protected very quickly[2].
[2] This describes a ‘standby’ level from which the responder can be fully protected in less than 2 minutes, but which is more comfortable and allows the responder to perform normal activities such as eating, drinking and using a toilet until required to be in full protection

Responders may be expected to don the PPE either before travelling or en route to an incident in a vehicle such as a Mercedes Sprinter van or a fire appliance. Responders will be expected to drive a variety of vehicles in the PPE, including cars, vans, goods and heavy goods vehicles, boats, underground trains and All Terrain Vehicles.

Whilst protection will not be sacrificed for speed of deployment, responders may need to dress quickly in the PPE on arrival at an incident. The removal of all normal clothing (for example to put on specialist undergarments) may be undesirable for modesty and time reasons and preparation or alteration of suits will also impact on this time imperative.

Responders will be expected to undertake essential activity very soon after arrival at a CBRN scene and will aim to create an environment where effective command and control can be undertaken. They will need to assess the hazardous environment and establish a cordon including setting up a cordon control point. They will expect to undertake casualty management including lifesaving (both medical and physical removal) and dealing with victims seeking assistance.

Responders can expect to deploy into an environment which may be physically hazardous including the potential for tear and puncture damage as well as for damaged and displaced items creating trip and other hazards. They will need to perform manual labour including digging, rescue activity moving cordon barriers and carrying other heavy equipment.

Responders can expect to use a variety of equipment[3] including (but not limited to) radios, mobile phones, computers, public communications equipment, detection identification and monitoring equipment, firearms, cutting equipment, medical equipment and tools. Some equipment will need a high degree of dexterity, such as use of a pipette, spatula, cannula or stylus. They may need to use a variety of safety equipment, for example for self-defence, protection or flotation.
[3] A full equipment list will be provided in any formal requirement showing the equipment and the level or priority attached to its use with the protective system.

Some responders may undertake physically demanding activities such as firearms operations, firefighting, urban search and rescue and military deployments and these require a high degree of flexibility of movement and dexterity.

There is the potential from an early stage for responders to become engaged in crowd control activity to establish order, arrest a suspect or provide assistance to distressed people. They may require protection to the level of existing protective equipment such as body armour and shoulder, arm and leg guards. This will also require them to be able to communicate decontamination/safe extraction processes, and to record (on video and in writing) details of people within and exiting the scene.

Some users may need to carry substantial personal equipment in a belt and/or back mounted system and this could be up to 45kg in weight.

Responders will need to be able to undress from the ensemble if uncontaminated, or to be safely extricated from it if contaminated in as short a time as possible. This will be required for responder casualties as well as to allow for rest periods.

Some responders may need to frequently cross the clean/dirty line, for example whilst handling exhibits, and may also need to remain forensically clean when moving from one area to another.

Responders can be expected to operate outside in the climatic conditions experienced within the UK[4], and, in some cases, throughout the world[5].
[4] UK climate extremes – temperature -27.2˚C to 38.5˚C. Met. Office website http://www.metoffice.gov.uk/public/weather/climate/?tab=climateExtremes
[5] Temperature -34˚C to 49˚C

Responders may be expected to operate in all types of locations and some examples are:
- open ground such as woods and fields and other rough or uneven terrain
- open urban areas such as streets, car parks, building sites, airport runways
- large structures such as sports facilities, shopping centres, industrial premises, public transport and freight hubs
- small and large buildings such as high-rise, houses, offices, sheds, garages, outbuildings and including gardens and yards
- public transport and vehicles including underground and overground trains, ships, aircraft, buses, lorries, vans, cars
- confined spaces[6] such as damaged or collapsed buildings, subsurface/ underground locations (including tube/metro/subway systems), small rooms, ships’ holds, storage facilities, cellars, caves, drains/sewers
  [6] A confined space is a place which is substantially enclosed (though not always entirely), and where serious injury can occur from hazardous substances or conditions within the space or nearby (e.g. lack of oxygen). HSE website, http://www.hse.gov.uk/confinedspace/
- working at height including line access, rooftops and other structures
- marine environments.

Responders will need to be deployed wearing the PPE continuously for varying periods; where these are extended they will need to eat, drink and use toilet facilities whilst retaining appropriate protection.

PPE that is not compliant with PPE Regulations for example because it is novel or aimed at a law enforcement or military application for which there is an exemption can be considered. However, compliance would be preferred and may be a requirement in the future.

Key User Requirements
The top 5 requirements are listed here but also included within the complete set in the next section.

ID	User Requirement
URD-3	The user shall be able to identify that the protection system is safe to use.
URD-8	The protection systems shall be uniquely marked to provide identification.
URD-32	The user shall be provided with a supply of safe air for the wear time duration whilst being protected in the environments referenced in the Activity-Environment matrix.
URD-34	The user shall be able to communicate verbally while protected with protected and unprotected individuals.
URD-35	The protection system shall provide the user with appropriate levels of whole body protection against the hazards defined in the M3PS Threat Spectrum reference.

User Requirements
ID	User Requirement	Priority	Measure of Effectiveness
N/A	Storage / These are the requirements for storage of the protection system before and after use.
URD-1	The user shall be able to store the protection system within a small volume when not in use.	HD	For Police, Fire and Health the threshold level is that the ensemble will fit within a 50 litre capacity holdall (approx dimensions 60x30x30 cm) and an objective level is that the ensemble will fit within a 30 litre capacity holdall (approx dimensions 50x30x30 cm)
URD-2	The user shall be able to store the protection system without reducing the effectiveness of the protection for a period of time.	HD	The protection system shall maintain protection levels in storage for a period of time. / Threshold level is 10 years. / Objectives level is 20 years.
URD-3	The user shall be able to identify that the protection system is safe to use.	K	Threshold - a visible identification to show whether the protective storage has been opened whilst stored. In addition to this a means of determining the length of time the system has been stored, whether it is within its expiry date and the length of time is has been used. / Objective - Manufacturer to provide a method by which the protection system can be checked it is still safe to use after previous uses.
URD-4	The user shall be able to store the protection system after use for reuse.	HD	The threshold and objective levels should be comparable to the shelf life figures referenced in URD-2. Manufacturer to provide a statement regarding these values.
URD-5	The system shall be usable once out of any protective packaging for a period of time.	HD	Threshold 2 years / Objective : 10 years
URD-6	The protection systems shall be packaged so as to allow users to store and transport them in bulk without effecting the protection levels of the ensembles.	HD	Ensure that it is possible to stack ensembles without effecting the protection levels. Manufacturers to provide statements as to how many can be stacked before protection levels are threatened.
URD-7	The protection systems shall be packaged so as to allow users to store them in a range of specified environments.	HD	Manufacturer to supply statement of storage conditions applicable and the effect of these on the equipment. / Threshold level is for the protection systems to be stored in climatically-controlled environments. Objective level is for the protection systems to be stored in non-climatically-controlled environments.
URD-8	The protection systems shall be uniquely marked to provide identification.	K	Required to show the expiry date (most important aspect), audit trail of production, audit trail of use, audit trail of issue of specific system components to specific individuals, size of system, maintenance log.
URD-9	The protection system protection levels shall be resistant to impact.	HD	Drop test to be performed from a defined height.
N/A	Transportation / These are the requirements for moving the protection systems to the required location.
URD-10	Each ensemble shall be portable by a single individual.	HD	To be measured against manual handling limits.
URD-11	The protection system shall be transportable internationally.	D	Pass or Fail. Manufacturer statement.
N/A	Don / These are the requirements for users to don the protection systems.
URD-12	The user shall be able to don the ensemble quickly to protected state. / Where don includes taking the protection system out of any protective storage.	HD	Threshold - 15 minutes. / Objective - 5 minutes.
URD-13	The user shall be able to don the ensemble over their normal work wear excluding any footwear. / Where don includes taking the protection system out of any protective storage	HD	Pass or Fail.
URD-14	The user shall be able to don the protection system at the scene with minimum user adjustments or assembly.	HD	To be measured against the don time figures reference in URD-12.
URD-15	The user shall be able to be visually checked by others that protection is donned correctly.	HD	Threshold level is a visual check at the scene.
URD-16	The user shall be able to don the ensemble within a restricted volume. / Where don includes taking the protection system out of any protective storage.	D	Threshold - respiratory protection can be donned within a police van. / Objective - complete ensemble can be donned within a police van.
URD-17	The user shall be able to don the ensemble quickly without assistance. / Where don includes taking the protection system out of any protective storage.	HD	Threshold - 15 minutes. / Objective - 5 minutes.
N/A	Standby State / These requirements outline the activities to be undertaken whilst in the Standby State.
URD-18	The protection system shall have a standby option for the user into which the user can move either from the undressed or the fully dressed state.	HD	Pass or Fail.
URD-19	The user shall be fully protected from standby status in less time than the full don time.	HD	Threshold - 2 minutes. / Objective - 1 minute.
N/A	Protected State / These requirements outline the activities to be undertaken whilst in the Protected State.
URD-20	The protection system shall allow the User to operate in a contaminated environment for prolonged and continuous periods.	HD	For all other agencies: / Threshold – 4 hours / Objective – 6 hours.
URD-21	The protection system shall provide the user with a short term protection option.	HD	Threshold - 30 minutes protection. / Objective - more than 30 minutes protection.
URD-22	The protection system shall allow the User to conduct normal bodily functions whilst fully protected.	HD	Pass or Fail.
URD-23	The protection system shall allow the User to drink without reducing the protection level whilst fully protected.	HD	Threshold level is for the user to be able to consume 500ml/min. / Objective level is for the user to be able to consume > 500ml/min.
URD-24	The protection system shall allow the User to drink and eat in an emergency.	HD	Pass or Fail.
URD-25	The protection system shall not hinder the ability to administer basic life support measures to the wearer.	HD	To be measured against ABC checks and possible countermeasures.
URD-26	The user shall have the provision for corrective vision.	HD	Pass or Fail.
URD-27	Whilst in the protected state it shall be possible to see the user’s face clearly.	HD	Threshold level is to be able to see the eyes of the user whilst in the fully dressed state. / Objective level is to be able to see the mouth of the user whilst in the fully dressed state.
URD-28	The user shall be able to stow items of equipment about their person.	HD	As a minimum a distress signal unit must be able to be attached to the user. Other equipment to be stowed to include DIM equipment, officer safety kit and a blade (for marine officers only).
URD-29	Whilst in the protected state it shall be possible for the user to see items on their own person.	D	Pass or Fail.
URD-30	Whilst in the protected state the user shall be able to hear surrounding noise.	HD	Signal to Noise Ratio to be defined for testing to ensure that users are able to hear the following representative noises: / Talking to other users / Personal alarms (pager, O2 meter, EPD/ RPD) / Auto distress signal units / Low pressure warning whistle on breathing apparatus / To be tested over a range of frequencies.
URD-31	Whilst in the protected state the user shall be able to maintain forensic cleanliness.	D	Materials of the protection system not able to contaminate the environment.
URD-32	The user shall be provided with a supply of safe air for the wear time duration whilst being protected in the environments referenced in the Activity-Environment matrix.	K	Pass or Fail.
URD-33	The supply of safe air shall have an indicator for the user indicating when the safety margin has been reached.	D	Threshold level is that this is provided for forced air supplies. / Objective level is that this is provided for all air supplies.
URD-34	The user shall be able to communicate verbally while protected with protected and unprotected individuals.	K	Pass or Fail.
N/A	Protection / These are the requirements for the protection levels required from the systems. The technical requirements specify these to greater detail.
URD-35	The protection system shall provide the User with appropriate levels of whole body protection against the hazards defined in the M3PS Threat Spectrum reference.	K	To be measured against the Threat Spectrum.
URD-36	The protection system shall be flame retardant.	HD	Threshold – protection no less than provided by daily working dress. / Objective – no thermal injury from the specified challenge. / Fire - Minimum criteria compliance with BS/EN requirements and structured testing
URD-37	The protection system shall be flame resistant.	HD	Threshold – protection no less than provided by daily working dress. / Objective – no thermal injury from the specified challenge.
URD-38	The protection system shall afford maximum resistance to wear and tear in the M3PS Activity-Environment matrix reference.	HD	Once removed from packaging the capability shall maintain protective level for not less than 36 hours and it should then be possible within the 36 hours to use the protection system with full protection for the user for a period of 6 hours (after which it will be replaced). / Included in this requirement is the ability to remove and redress in the protection system 10 within this timeframe.
URD-39	Whilst in the protection system the user shall be able to perform the activities referenced in the M3PS Activity-Environment matrix reference within the environmental conditions specified.	HD	To be measured against the activity-environment matrix referenced.
URD-40	Whilst in the protection system the user shall be protected from conducted heat and cold in all operational environments as defined in the M3PS Activity-Environment matrix reference.	D	To be measure against wear time figures referenced in URD-20 when undertaking relevant operational activities.
URD-41	Whilst in the protection system the user shall be protected from tear, cut and puncture from sharp objects.	HD	To be measured against wear time figures referenced in URD-20 when undertaking relevant operational activities.
URD-42	Whilst in the protection system the user shall be protected from sharp objects on the soles and toes.	HD	Pass or Fail in line with footwear standards.
URD-43	Whilst in the protection system the user shall be protected from hand injuries from sharp objects.	HD	Pass Fail in line with the relevant gloves standards.
URD-44	Whilst in the protection system the user shall be protected from loud noises.	D	The threshold level is that it is possible to wear ear defenders with the protection system.
N/A	Decontaminate/ Disrobe / These are the requirements for users to decontaminate and/ or disrobe the protection systems.
URD-45	The protection system shall be compatible with in-service decontaminants.	HD	Threshold - The system performance shall not be degraded when exposed to in-service decontaminants / Objective - The system performance shall be enhanced when exposed to in-service decontaminants.
URD-46	The user shall be able to safely undress in under 10 minutes.	HD	Threshold: 10 minutes. / Objective: 2 minutes.
URD-47	The user shall be able to emergency disrobe without assistance.	HD	Pass or Fail.
N/A	Dispose / These are the requirements for the disposal of the protection systems.
URD-48	The supplier shall provide a solution for disposal of un-contaminated protection systems.	M	Pass or Fail.
N/A	Re-Use / These are the requirements for re-use of the protection systems which will only occur if the protection systems are uncontaminated.
URD-49	The protection systems shall be reusable after use in an uncontaminated environment.	HD	Threshold level is three or more wears / Objective level is 10 or more wears.
N/A	Maintenance / These are the requirements relating to the maintenance of the protection systems.
URD-50	The system supplier shall provide a method of testing that the system’s protection is still effective.	HD	Supplier statement.
URD-51	The system supplier shall provide support when testing the effectiveness of protection.	HD	Pass or Fail.
URD-52	The system supplier shall provide support for maintenance of the system.	HD	Pass or Fail.
URD-53	A suitably trained user shall be able to maintain the system.	HD	Pass or Fail.
N/A	Training / These are the requirements relating to user training of the use of the protection systems.
URD-54	The protection system shall present the User with the minimum training burden.	HD	Supplier to provide train the trainer package.
N/A	Look and Feel / These requirements outline the design principles for the protection systems and are applicable to the protection systems regardless of the state of dress.
URD-55	The protection system shall not present the User with a snagging hazard.	HD	To ensure that the ensembles do not include any flaps, straps or material fold that could pose a snagging hazard.
URD-56	The protection system shall not present the User with a dermatological irritant.	M	Statement from manufacturer. To not include any materials with skin notation in EH40.
URD-57	The protection system shall have provision for displaying individual recognition insignia.	HD	Pass or Fail.
URD-58	The protection system shall be available in in-service camouflage pattern (MTP).	HD	Pass or Fail.
URD-59	The protection system shall be available in a colour compatible with Emergency Service systems.	HD	Pass or Fail.
URD-60	The protection system shall be coloured according to service.	D	Pass or Fail.
URD-61	The protection system shall be usable as everyday clothing or uniform.	D	Pass or Fail.
URD-62	The protection system shall make specific provision for right and left handed users.	D	Pass or Fail.
URD-63	The protection systems shall fit a range of user sizes including male and female.	M	To be able to fit individuals within the 5th and 95th percentile of the population.
URD-64	The protection system shall provide grip for the user on icy and wet surfaces.	HD	Pass or Fail in line with footwear standards.
URD-65	The user shall be informed by the system as to their physiological condition.	D	Threshold information to be core body temperature of the user.
URD-66	The command centre shall be informed by the system as to the user's physiological condition.	D	Threshold information to be core body temperature of the user.
URD-67	The user shall be informed by the system as to the surrounding environment.	D	To be measured against the materials within the threat spectrum provided.
URD-68	The user shall be warned by the system if the surrounding environment poses a hazard.	D	To be measured against the materials within the threat spectrum provided.
N/A	Environmental / These are the requirements relating to the environments in which the protection systems are expected to protect the user.
URD-69	The user shall be able to operate whilst protected for extended periods of time without excessive physiological burden when in a range of operational environments and performing a range of activities as specified within the M3PS Activity-Environment matrix reference.	HD	Physiological burden for the user to be minimal for the duration of the wear time whilst conducting the activities listed in the Activity-Environment matrix and whilst operating in the relevant Operational Environments as indicated within the Activity-Environment matrix.
URD-70	The protection system shall provide the user with contamination protection when wet (water).	HD	Threshold - 0.8 mm/min for 4 hours / Objective - 3.13 ml/min for 6 hours. / It is the objective that this covers salt water as well as non-salt water.
URD-71	The protection system shall operate effectively when contaminated with petrol, oil and lubricants (POL).	D	Supplier statement.
N/A	Equipment Inter-Operability / These requirements outline the other equipment to be used by the user whilst wearing the protection system.
URD-72	Whilst in the protected state the user shall be able to operate equipment without affecting the operation of the equipment or the level of protection provided by the protection system as referenced in the M3PS Equipment List reference.	HD	Pass or Fail for the range of equipment.
URD-73	The protection system either shall incorporate the provision of or shall be compatible with in-service apparatus supplying uncontaminated air.	HD	List of equipment to be provided
URD-74	The user shall be able to wear protection equipment in addition to the protection system without affecting the effectiveness of the additional protection equipment or the protection provided by the protection system as referenced in the M3PS Equipment List.	HD	Pass or Fail for the range of equipment.
N/A	Service Inter-Operability / These are the requirements that enable all the services (Fire, Health, Police, MoD) to work together efficiently at the scene.
URD-75	The donning process for the protection systems shall be common across all services.	HD	Pass or Fail.
URD-76	The disrobing process for the protection systems shall be common across all services.	HD	Pass or Fail.
URD-77	The safe undressing process for the protection systems shall be common across all services.	HD	Pass or Fail.
URD-78	The emergency disrobe process for the protection systems shall be common across all services.	HD	Pass or Fail.
URD-79	Whilst protected users from all services shall be able to communicate.	HD	Pass or Fail.
URD-80	Sizing of the protection systems shall be common across all services.	HD	Pass or Fail.
URD-81	Task identification of the users shall be common across all services.	HD	Pass or Fail.
N/A	Standards / These are the standards that the protection systems are required to comply to and are expanded further within the technical requirements.
URD-82	The protection system shall generate minimum static discharge.	HD	To meet specified standards.
URD-83	The protection systems shall be resistant to interference from other devices including deliberate action.	HD	Pass or Fail.
URD-84	The protection systems shall be intrinsically safe.	HD	Pass or Fail.
URD-85	The protection system shall be CE marked by the time of supply.	M	Manufacturer to supply statement of CE marking or detailed evidence to show that the CE marking process is underway. The supplier shall ensure that the configuration submitted for evaluation shall be the same configuration as submitted for CE marking. / Any notified body used for CE marking shall be accredited.

Glossary of Terms
Term	Definition
Contaminated Environment	Any environment in which a hazardous material is present.
Decontaminate	The process by which a person or object has contamination removed.
Disrobe	The term used to describe the removal of the protection system from the user when the protection system is not contaminated.
Don	The term used to describe the user putting on the protection system.
Donning Process	The process by which the user puts on the protection system including any time taken to remove from packaging and prepare for wear.
Emergency Disrobe	The term used to describe a faster removal of the protection system from the user when the user is in discomfort and at risk.
Ensemble	Within the MP3S complete system it is envisaged that there will be components which when worn together will form an ensemble to provide the appropriate protection for the threat level.
Fully dressed	This is where the user is wearing the full ensemble appropriate for the threat level.
Protected	The term used to describe the user when in the full dress state of the protection system appropriate for the threat level.
Individual Recognition Insignia	These vary across the agencies but typically identify the agency, force, rank and identification of the individual user.
MP3S Activity-Environment Matrix	This is a reference to the activities required to be undertaken by the users whilst in the protection system and within the relevant environments.
MP3S Equipment List	This is a reference to the equipment to be used by users whilst in the protection system.
Normal Work wear	This will vary across the agencies.
Objective	Desired measurement of effectiveness.
Protected State	The term used to describe the full dress state of the protection system.
Protection Equipment	This covers all equipment that users have for protection over and above the protection system.
Protection System	This includes the entire suite of options within the system to fulfil the user protection against the threat spectrum. This will include a variety of dermal and respiratory protection for the entire body as required to protect the user from the identified threats.
Protective Packaging	This relates to any packaging required for the protection system to maintain its protection levels during storage or transportation.
Safely Undress	The term used to describe the removal of the protection system from the user when the protection system is contaminated.
Standby	The term used to describe a lesser dress state in order to reduce the time taken for the user to become fully protection and to reduce the physiological burden whilst waiting to enter the scene.
Task Identification	The tasks undertaken by the users can be consolidated and should be identifiable to other users regardless of the agency the user belongs to.
Threshold	Minimum acceptable measurement of effectiveness.
Uncontaminated Environment	This is an environment in which there are no threats present.
Uncontaminated Protection Systems	These are protection system which have not been in a contaminated environment or have been suitably decontaminated.
Undressed	This is where the user is not wearing any element of the MP3S.
Unprotected Individuals	These are individuals within the scene that are not wearing a protection system and are likely to be members of the public.
Whole Body Protection	Ensuring the user is fully protected from the threat e.g. if it is a respiratory threat only, whole body protection will be provided by ensuring the user has a safe supply of air.