Notice of variation and consolidation with introductory note

The Environmental Permitting (England & Wales) Regulations 2010

Sheardown Farms Limited

Green Lane Poultry Unit

Mill Lane

Orston

Nottinghamshire

NG13 9NE

#### Variation application number

EPR/ZP3433ZP/V004

#### Permit number

EPR/ZP3433ZP

# Green Lane Poultry Unit 
Permit number EPR/ZP3433ZP

## Introductory note

### This introductory note does not form a part of the notice

Under the Environmental Permitting (England & Wales) Regulations 2016 (schedule 5, part 1, paragraph 19) a variation may comprise a consolidated permit reflecting the variations and a notice specifying the variations included in that consolidated permit.

Schedule 1 of the notice specifies the conditions that have been varied and schedule 2 comprises a consolidated permit which reflects the variations being made. Only the variations specified in schedule 1 are subject to a right of appeal.

This variation authorises the following changes:

- The increase in permitted capacity from 410,000 to 450,000 broilers

- The addition of one 1.07MW Biomass boiler to the other 12 existing biomass boilers on site.

- The renumbering of existing poultry houses

- The addition of 2 new poultry houses, numbered House 9 and House 10

2 houses (House 7 and House 8) proposed in the last variation, EPR/ZP3433ZP/V003, were not built. Due to the renumbering of the houses these will now be built and named House 9 and House 10. The location of these new houses has changed, see the site plan in Schedule 7 of this notice.

There are no other changes as a result of this variation.

The main features of the installation are:

Green Lane Farm is situated in open countryside approximately 1 km north east of the village of Orston, Nottinghamshire. The installation is approximately centred on National Grid Reference SK 77800 41800. The nearest receptor is the farm dwelling, approximately 55 metres north-east of the north-eastern edge of Poultry house 1. Lodge Farm is approximately 470 metres to the south-east of Poultry house 5 and 6.  A Pavilion and sports ground is 585 metres to the south-west of Poultry house 5 and 6.

The installation is operated by Sheardown Farms Limited and comprises ten broiler houses. The total permitted livestock on the installation is 450,000 broiler chickens.

Poultry houses are ventilated by side wall inlets and high velocity roof fan outlets. These houses also have gable end fans, although these are operated infrequently to maintain temperature, typically in the summer months.

At the beginning of the crop cycle, bedding is spread on the floors and the houses are pre-warmed using space heaters fuelled by biomass boilers.  Day old birds are brought onto the farm and as the birds grow the temperature is gradually reduced and the ventilation is increased. At 35 days a proportion of the birds are removed for slaughter, with the remainder being processed at approximately 41/42 days of age.

At the end of the cycle the houses are depopulated, washed and disinfected ready for the next cycle. The used litter is removed by a third party contractor for spreading on land owned by third parties or for power regeneration. Water from the wash out of poultry houses is channelled to underground collection tanks close to the houses to await export off site and spread on land owned by third parties.

During normal operations, roof water from all poultry houses drains to an attenuation pond via French drains located at the sides of each building and ultimately drains to the River Smite. Clean surface water from the concrete aprons at the end of all houses is discharged to the attenuation pond via covered drains and a diverter valve. In the event that this water is contaminated it is diverted to the underground collection tanks.

Mortalities are collected daily and stored in a secure container on site for removal under the National Fallen Stock Scheme. Associated food is stored on the installation in sealed food bins.

#### There is one Site of Special Scientific Interest (SSSI) located within 5 km of the site and seven Local Wildlife Sites (LWS) located within 2 km of the site.

An assessment of the impact of emissions has been carried out and the installation is considered to have no adverse effect on the nature conservation sites.

The schedules specify the changes made to the permit.

The status log of a permit sets out the permitting history, including any changes to the permit reference number.

| Status log of the permit |
| --- |
| Description | Date | Comments |
| Application EPR/ZP3433ZP/A001 | Duly made 31/08/12 | Application for an intensive farming poultry installation permit. |
| Additional information received | 29/10/12 | Confirmation of number of houses and number of birds and details of future development. |
| Permit determined EPR/ZP3433ZP | 20/11/12 | Permit issued to Sheardown Farms Limited. |
| Variation application EPR/ZP3433ZP/V002 | 10/01/14 | Application to vary the permit to install 4 biomass boilers and update the permit to modern conditions to include the requirements of IED. |
| Additional information received | 03/03/14 | Further clarification of biomass boiler fuel storage accident prevention measures. |
| Variation issued EPR/ZP3433ZP/V002 | 24/03/14 | Varied and consolidated permit issued in modern condition format. |
| Variation application EPR/ZP3433ZP/V003 | 21/10/14 | Application to add 6 Poultry Houses,12 biomass boilers and increase the permitted capacity from 310,000 to 410,000 broiler |
| Response to request for additional information dated 30/10/14 | 06/11/14 | Details of roof ridge heights and Oxygen content of pollutant emissions. |
| Response to request for additional information dated 30/10/14 | 10/11/14 | Details of Biomass boiler specifications by location together with RHI certificate for additional specification. |
| Response to request for additional information dated 20/11/14 | 01/12/14 | Amended site plan. |
| Variation determined EPR/ZP3433ZP/V003 | 18/12/14 | Varied and consolidated permit issued. |
| Variation application EPR/ZP3433ZP/V004 | Duly Made 19/06/17 | Application to vary the permit to install one biomass boiler and increase number of broilers from 410,000 to 450,000. Also increase number of houses from 8 to 10 and renumbering of houses. |
| Response to request for additional information dated 14/06/17 | 15/06/17 | Confirmation of thermal input of new biomass boiler and location of sensitive receptors. Submission of updated: odour management plan, Non-technical summary, emergency fire procedure. |
| Response to request for additional information dated 14/06/17 | 19/06/17 | Submission of Dust and Bio-aerosol Risk Assessment and Management Plan. |
| Response to request for additional information dated 24/07/17 | 26/07/17 | Response to Schedule 5 regarding biomass boiler specifications and confirmation on existing and proposed poultry housing. |
| Response to request for additional information dated 07/09/17 | 07/09/17 | Submission of amended Noise Management Plan and Drainage Plan |
| Variation determined EPR/ZP3433ZP/V004 (Billing Reference: DP3435YU) | 11/09/17 | Varied and consolidated permit issued. |

End of introductory note

## Notice of variation and consolidation

### The Environmental Permitting (England and Wales) Regulations 2016

The Environment Agency in exercise of its powers under regulation 20 of the Environmental Permitting (England and Wales) Regulations 2016 varies

#### Permit number

EPR/ZP3433ZP

#### Issued to

Sheardown Farms Limited (“the operator”)

whose registered office is

15 Newland

Lincoln

Lincolnshire

LN1 1XG

company registration number 03743291

to operate a regulated facility at

Green Lane Poultry Unit

Mill Lane

Orston

Nottinghamshire

NG13 9NE

to the extent set out in the schedules.

The notice shall take effect from 11/09/2017.

| Name | Date |
| --- | --- |
| Mike Jenkins | 11/09/2017 |

Authorised on behalf of the Environment Agency

#### Schedule 1

All conditions have been varied by the consolidated permit EPR/ZP3433ZP as a result of the application made by the operator.

#### Schedule 2 – consolidated permit

Consolidated permit issued as a separate document.

## Permit

### The Environmental Permitting (England and Wales) Regulations 2016

#### Permit number

EPR/ZP3433ZP

This is the consolidated permit referred to in the variation and consolidation notice for application EPR/ZP3433ZP/V004 authorising,

Sheardown Farms Limited (“the operator”),

whose registered office is

15 Newland

Lincoln

Lincolnshire

LN1 1XG

company registration number 03743291

to operate an installation at

Green Lane Poultry Unit

Mill Lane

Orston

Nottinghamshire

NG13 9NE

to the extent authorised by and subject to the conditions of this permit.

| Name | Date |
| --- | --- |
| Mike Jenkins | 11/09/2017 |

Authorised on behalf of the Environment Agency

# Conditions

- Management

  - General management

    - The operator shall manage and operate the activities:

      - in accordance with a written management system that identifies and minimises risks of pollution, so far as is reasonably practicable, including those risks arising from operations, maintenance, accidents, incidents, non-conformances, closure and those drawn to the attention of the operator as a result of complaints; and

      - using sufficient competent persons and resources.

    - Records demonstrating compliance with condition 1.1.1 shall be maintained.

    - Any person having duties that are or may be affected by the matters set out in this permit shall have convenient access to a copy of the permit.

  - Energy efficiency

    - The operator shall:

      - take appropriate measures to ensure that energy is used efficiently in the activities;

      - maintain records of fuel and energy consumption used in the activities;

  - Efficient use of raw materials

    - The operator shall:

- (a)	take appropriate measures to ensure that raw materials and water are used efficiently in the    activities; and

- (b) maintain records of raw materials and water used in the activities;

Avoidance, recovery and disposal of wastes produced by the activities

    - The operator shall take appropriate measures to ensure that the waste hierarchy referred to in Article 4 of the Waste Framework Directive is applied to the generation of waste by the activities and that;

      - any waste generated by the activities is treated in accordance with the waste hierarchy referred to in Article 4 of the Waste Framework Directive; and

      - where disposal is necessary, this is undertaken in a manner which minimises its impact on the environment.

- Operations

  - Permitted activities

    - The only activity authorised by the permit is the activity specified in schedule 1 table S1.1 (the “activities”).

  - The site

    - The activities shall not extend beyond the site, being the land shown edged in green on the site plan at schedule 7 to this permit.

  - Operating techniques

    - The activities shall, subject to the conditions of this permit, be operated using the techniques and in the manner described in the documentation specified in schedule 1, table S1.2, unless otherwise agreed in writing by the Environment Agency.

    - If notified by the Environment Agency that the activities are giving rise to pollution, the operator shall submit to the Environment Agency for approval within the period specified, a revision of any plan or other documentation (“plan”) specified in schedule 1, table S1.2 or otherwise required under this permit which identifies and minimises the risks of pollution relevant to that plan, and shall implement the approved revised plan in place of the original from the date of approval, unless otherwise agreed in writing by the Environment Agency.

    - The operator shall maintain and implement a system to record the number of animal places and animal movements.

    - The operator shall ensure that a diet formulation and nutritional strategy is used to reduce the total nitrogen and total phosphorous excreted.

    - The operator shall take appropriate measures in disposal or recovery of solid manure or slurry to prevent, or where this is not practicable, to minimise pollution.

    - Any raw materials or fuels listed in schedule 2 table S2.1 shall conform to the specifications set out in that table.

The operator shall ensure that where waste produced by the activities is sent to a relevant waste operation, that operation is provided with the following information, prior to the receipt of the waste:

the nature of the process producing the waste;

the composition of the waste;

the handling requirements of the waste;

the hazardous property associated with the waste, if applicable; and

the waste code of the waste.

- Emissions and monitoring

  - Emissions to water, air or land

    - There shall be no point source emissions to water, air or land except from the sources and emission points specified in table S3.1 and S3.2.

    - The limits given in schedule 3 shall not be exceeded.

3.1.3	Periodic monitoring shall be carried out at least once every 5 years for groundwater and 10 years for soil, unless such monitoring is based on a systematic appraisal of the risk of contamination.

  - Emissions of substances not controlled by emission limits

    - Emissions of substances not controlled by emission limits shall not cause pollution. The operator shall not be taken to have breached this condition if appropriate measures, including, but not limited to, those specified in any approved emissions management plan, have been taken to prevent or where that is not practicable, to minimise, those emissions.

    - The operator shall:

      - if notified by the Environment Agency that the activities are giving rise to pollution, submit to the Environment Agency for approval within the period specified, an emissions management plan which identifies and minimises the risks of pollution from emissions of substances not controlled by emission limits; and

      - implement the approved emissions management plan, from the date of approval, unless otherwise agreed in writing by the Environment Agency.

    - All liquids in containers, whose emission to water or land could cause pollution, shall be provided with secondary containment, unless the operator has used other appropriate measures to prevent or where that is not practicable, to minimise, leakage and spillage from the primary container.

  - Odour

    - Emissions from the activities shall be free from odour at levels likely to cause pollution outside the site, as perceived by an authorised officer of the Environment Agency, unless the operator has used appropriate measures, including, but not limited to, those specified in any approved odour management plan, to prevent or where that is not practicable to minimise the odour.

  - Noise and vibration

    - Emissions from the activities shall be free from noise and vibration at levels likely to cause pollution outside the site, as perceived by an authorised officer of the Environment Agency, unless the operator has used appropriate measures, including, but not limited to, those specified in any approved noise and vibration management plan to prevent or where that is not practicable to minimise the noise and vibration.

  - Monitoring

    - The operator shall, unless otherwise agreed in writing by the Environment Agency, undertake the monitoring specified in the following tables in schedule 3 to this permit:

      - point source emissions specified in tables S3.1 and S3.2;

  - Pests

    - The activities shall not give rise to the presence of pests which are likely to cause pollution, hazard or annoyance outside the boundary of the site. The operator shall not be taken to have breached this condition if appropriate measures, including, but not limited to, those specified in any approved pests management plan, have been taken to prevent or where that is not practicable, to minimise the presence of pests on the site.

    - The operator shall:

      - if notified by the Environment Agency, submit to the Environment Agency for approval within the period specified, a pests management plan which identifies and minimises risks of pollution, hazard or annoyance from pests; and

      - implement the pests management plan, from the date of approval, unless otherwise agreed in writing by the Environment Agency.

- Information

  - Records

    - All records required to be made by schedules 3, 4 and 5 to this permit shall:

      - be legible;

      - be made as soon as reasonably practicable;

      - if amended, be amended in such a way that the original and any subsequent amendments remain legible, or are capable of retrieval; and

      - be retained, unless otherwise agreed in writing by the Environment Agency, for at least 6 years from the date when the records were made, or in the case of the following records until permit surrender:

        - off-site environmental effects; and

        - matters which affect the condition of the land and groundwater.

    - The operator shall maintain convenient access, in either electronic or hard copy, to the records, plans and management system required to be maintained by this permit.

  - Reporting

    - The operator shall send all reports and notifications required by the permit to the Environment Agency using the contact details supplied in writing by the Environment Agency.

    - For the following activities referenced in schedule 1, table S1.1 a report or reports on the performance of the activities over the previous year shall be submitted to the Environment Agency by 31 January (or other date agreed in writing by the Environment Agency) each year. The report(s) shall include as a minimum:

      - a review of the results of the monitoring and assessment carried out in accordance with the permit including an interpretive review of that data.

    - The operator shall, unless notice under this condition has been served within the preceding four years, submit to the Environment Agency, within six months of receipt of a written notice, a report assessing whether there are other appropriate measures that could be taken to prevent, or where that is not practicable, to minimise pollution.

  - Notifications

    - In the event:

      - that the operation of the activities gives rise to an incident or accident which 	significantly affects or may significantly affect the environment, the operator must immediately :—

        - inform the Environment Agency,

        - take the measures necessary to limit the environmental consequences of such an incident or accident, and

        - take the measures necessary to prevent further possible incidents or accidents; and

      - of a breach of any permit condition the operator must immediately :—

        - inform the Environment Agency, and

        - take the measures necessary to ensure that compliance is restored within the shortest possible time;and

      - of a breach of permit condition which poses an immediate danger to human health or threatens to cause an immediate significant adverse effect on the environment, the operator must immediately suspend the operation of the activities or the relevant part of it until compliance with the permit conditions has been restored.

    - Any information provided under condition 4.3.1 shall be confirmed by sending the information listed in schedule 5 to this permit within the time period specified in that schedule.

    - Where the Environment Agency has requested in writing that it shall be notified when the operator is to undertake monitoring and/or spot sampling, the operator shall inform the Environment Agency when the relevant monitoring and/or spot sampling is to take place. The operator shall provide this information to the Environment Agency at least 14 days before the date the monitoring is to be undertaken.

    - The Environment Agency shall be notified within 14 days of the occurrence of the following matters, except where such disclosure is prohibited by Stock Exchange rules:

Where the operator is a registered company:

      - any change in the operator’s trading name, registered name or registered office address; and

      - any steps taken with a view to the operator going into administration, entering into a company voluntary arrangement or being wound up.

Where the operator is a corporate body other than a registered company:

      - any change in the operator’s name or address; and

      - any steps taken with a view to the dissolution of the operator.

In any other case:

      - the death of any of the named operators (where the operator consists of more than one named individual);

      - any change in the operator’s name(s) or address(es); and

      - any steps taken with a view to the operator, or any one of them, going into bankruptcy, entering into a composition or arrangement with creditors, or, in the case of them being in a partnership, dissolving the partnership.

    - Where the operator proposes to make a change in the nature or functioning, or an extension of the activities, which may have consequences for the environment and the change is not otherwise the subject of an application for approval under the Regulations or this permit:

      - the Environment Agency shall be notified at least 14 days before making the change; and

      - the notification shall contain a description of the proposed change in operation.

    - The Environment Agency shall be given at least 14 days notice before implementation of any part of the site closure plan.

  - Interpretation

    - In this permit the expressions listed in schedule 6 shall have the meaning given in that schedule.

    - In this permit references to reports and notifications mean written reports and notifications, except where reference is made to notification being made “immediately”, in which case it may be provided by telephone.

# Schedule 1 – Operations

| Table S1.1 activities |
| --- |
| Activity listed in Schedule 1 of the EP Regulations | Description of specified activity | Limits of specified activity |
| Section 6.9 A(1)(a)(i) Rearing of poultry intensively in an installation with more than 40,000 places | The rearing of poultry in a facility with a capacity for 450,000 broiler places. | From receipt of birds, raw materials and fuels onto the site to removal of birds and associated wastes from site. |
| Directly Associated Activity | Description of specified activity | Limits of specified activity |
| Biomass boiler | Operation of 13 biomass boilers with an aggregated thermal rated input not exceeding 3.72 MWth, for site heating requirements, burning biomass fuel not comprising waste or animal carcasses. | From receipt of raw materials and fuels, to release of combustion products to air and associated wastes removed from site. |
| Table S1.2 Operating techniques |
| Description | Parts | Date Received |
| Application EPR/ZP3433ZP/A001 | Responses to Part B3 section 3 of the application form and referenced supporting documentation, including odour management plan, noise management plan, non-technical summary and housing and drainage plan. | 03/09/12 |
| Request for Information dated 29/10/12 | Confirmation of number of houses, number of birds and details of future development. | 29/10/12 |
| Request for Information dated 30/10/12 | Confirmation that House 5 should not be included in the permit conditions (not included on the Housing and Drainage plan or Schedule 3 – emissions and monitoring). | 30/10/12 |
| Application EPR/ZP3433ZP/V002 | Responses to Parts C2 and C3 of the application form and referenced supporting documentation. | 10/01/14 |
| Additional information requested 27/02/14 | Response to Request for Information clarifying poultry house ventilation, pre-operational condition removal, site drainage, biomass boiler fuel storage accident prevention measures and biomass boiler ash disposal. | 02/03/14 |
| Additional information requested 03/03/14 | Response to Request for Information further clarifying biomass boiler fuel storage accident prevention measures. | 03/03/14 |
| Application EPR/ZP3433ZP/V003 | Responses to Parts C2 and C3 of the application form and referenced supporting documentation including amended odour management plan, noise management plan and fugitive emission management plan. | 21/10/14 |
| Additional information requested 30/10/14 | Details of roof ridge heights and Oxygen concentrations of pollutant emissions | 06/11/14 |
| Additional information requested 30/10/14 | Details of Biomass boiler specifications by location together with RHI certificate for additional specification | 10/11/14 |
| Application EPR/ZP3433ZP/V004 | Responses to Parts C2 and C3.5 of the application form and referenced supporting documentation including amended dust management plan. | 19/04/17 |
| Additional information requested 14/06/17 | Response to Request for Information on amended odour management plan and emergency fire procedure. | 15/06/17 |
| Additional information requested 14/06/17 | Response to Request for Information on amended Dust and Bio-aerosol Risk Assessment and Management Plan. | 19/06/17 |
| Additional information requested 24/07/17 | Response to Request for Information clarifying the locations of existing housing and proposed variation. | 26/07/17 |
| Additional information requested 07/09/17 | Response to Request for Information on amended Noise Management Plan and Drainage Plan | 07/09/17 |

# Schedule 2 – Waste types, raw materials and fuels

| Table S2.1 Raw materials and fuels |
| --- |
| Raw materials and fuel description | Specification |
| Fuel for biomass boiler units | Biomass pellets comprising virgin timber, straw, miscanthus or a combination of these. |

# Schedule 3 – Emissions and monitoring

| Table S3.1 Point source emissions to air – emission limits and monitoring requirements |
| --- |
| Emission point ref. & location | Source | Parameter | Limit (including unit) | Reference Period | Monitoring frequency | Monitoring standard or method |
| High velocity roof fan outlets on poultry houses 1-10 shown on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Poultry houses 1-10 | --- | --- | --- | --- | --- |
| Gable end fan outlets on poultry houses 1-10 as shown on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Poultry houses 1-10 | --- | --- | --- | --- | --- |
| Exhaust from generator as shown on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Generator | --- | --- | --- | --- | --- |
| Vent from oil tank as shown on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Diesel tank | --- | --- | --- | --- | --- |
| Emissions from 13 biomass boilers as shown on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Aggregated 3.72 MWth biomass boilers | --- | --- | --- | --- | --- |

| Table S3.2 Point Source emissions to water (other than sewer) and land – emission limits and monitoring requirements |
| --- |
| Emission point ref. & location | Source | Parameter | Limit (incl. unit) | Reference Period | Monitoring frequency | Monitoring standard or method |
| Outlet to surface water west of poultry house 1, via attenuation pond, which drains to the River Smite as indicated on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Roof water from poultry houses 1-10 intercepted by French drains and attenuation pond prior to discharge (excluding poultry house wash out periods) | --- | --- | --- | --- | --- |
| Outlet to surface water west of poultry house 1, via attenuation pond, which drains to the River Smite as indicated on ‘GRNp02 Site Layout Plan v2’ in Schedule 7. | Yard surface water from concrete aprons at the ends of poultry houses 1 - 10 (excluding poultry house wash out periods) | --- | --- | --- | --- | --- |

# Schedule 4 – Reporting

There is no reporting under this schedule.

# Schedule 5 – Notification

These pages outline the information that the operator must provide.

Units of measurement used in information supplied under Part A and B requirements shall be appropriate to the circumstances of the emission. Where appropriate, a comparison should be made of actual emissions and authorised emission limits.

If any information is considered commercially confidential, it should be separated from non-confidential information, supplied on a separate sheet and accompanied by an application for commercial confidentiality under the provisions of the EP Regulations.

## Part A

| Permit Number |  |
| --- | --- |
| Name of operator |  |
| Location of Facility |  |
| Time and date of the detection |  |
| (a) Notification requirements for any malfunction, breakdown or failure of equipment or techniques, accident, or emission of a substance not controlled by an emission limit which has caused, is causing or may cause significant pollution |
| To be notified within 24 hours of detection |
| Date and time of the event |  |
| Reference or description of the location of the event |  |
| Description of where any release into the environment took place |  |
| Substances(s) potentially released |  |
| Best estimate of the quantity or rate of release of substances |  |
| Measures taken, or intended to be taken, to stop any emission |  |
| Description of the failure or accident. |  |
| (b) Notification requirements for the breach of a limit |
| To be notified within 24 hours of detection |
| Emission point reference/ source |  |
| Parameter(s) |  |
| Limit |  |
| Measured value and uncertainty |  |
| Date and time of monitoring |  |
| Measures taken, or intended to be taken, to stop the emission |  |

| Time periods for notification following detection of a breach of a limit |
| --- |
| Parameter | Notification period |
| (c) Notification requirements for the detection of any significant adverse environmental effect |
| To be notified within 24 hours of detection |
| Description of where the effect on the environment was detected |  |
| Substances(s) detected |  |
| Concentrations of substances detected |  |
| Date of monitoring/sampling |  |

## Part B – to be submitted as soon as practicable

| Any more accurate information on the matters for notification under Part A. |  |
| --- | --- |
| Measures taken, or intended to be taken, to prevent a recurrence of the incident |  |
| Measures taken, or intended to be taken, to rectify, limit or prevent any pollution of the environment which has been or may be caused by the emission |  |
| The dates of any unauthorised emissions from the facility in the preceding 24 months. |  |
| Name* |  |
| Post |  |
| Signature |  |
| Date |  |

* authorised to sign on behalf of the operator

# Schedule 6 – Interpretation

“accident” means an accident that may result in pollution.

“application” means the application for this permit, together with any additional information supplied by the operator as part of the application and any response to a notice served under Schedule 5 to the EP Regulations.

“authorised officer” means any person authorised by the Environment Agency under section 108(1) of The Environment Act 1995 to exercise, in accordance with the terms of any such authorisation, any power specified in section 108(4) of that Act.

“building” means a construction that has the objective of providing sheltering cover and minimising emissions of noise, particulate matter, odour and litter.

“emissions to land” includes emissions to groundwater.

“emissions of substances not controlled by emission limits” means emissions of substances to air, water or land from the activities, either from the emission points specified in schedule 3 or from other localised or diffuse sources, which are not controlled by an emission limit.

“groundwater” means all water, which is below the surface of the ground in the saturation zone and in direct contact with the ground or subsoil.

“Hazardous property” has the meaning in Annex lll of the Waste Framework Directive.

“Industrial Emissions Directive” means DIRECTIVE 2010/75/EU OF THE EUROPEAN PARLIAMENT AND OF THE COUNCIL of 24 November 2010 on industrial emissions.

“List of Wastes” means the list of wastes established by Commission Decision 2000/532/EC replacing Decision 94/3/EC establishing a list of wastes pursuant to Article 1(a) of Council Directive 75/442/EEC on waste and Council Decision 94/904/EC establishing a list of hazardous waste pursuant to Article 1(4) of Council Directive 91/689/EEC on hazardous waste, as amended from time to time.

“virgin timber” means timber from

Whole trees and the woody parts of trees including branches and bark derived from forestry works, woodland management, tree surgery and other similar operations (it does not include clippings or trimmings that consist primarily of foliage);

Virgin wood processing (e.g. wood offcuts, shavings or sawdust from sawmills) or timber product manufacture dealing in virgin timber.

If virgin timber is mixed with waste timber or any other waste, the mixed load is classed as waste.

“pests” means Birds, Vermin and Insects.

“Waste code” means the six digit code referable to a type of waste in accordance with the List of Wastes and in relation to hazardous waste, includes the asterisk

“Waste Framework Directive” or “WFD” means Waste Framework Directive 2008/98/EC of the European Parliament and of the Council on waste.

“year” means calendar year ending 31 December.

# Schedule 7 – Site plan

Site Location Map

©Crown Copyright. All rights reserved. Environment Agency, 100024198, 2017.

END OF PERMIT